## Slide 1: I4
SUNHOKEY

## Slide 2: step1:Unscrew 4pcs of screws to take the heatbed apart from the base

## Slide 3: after step1 finishes, it looks like below

## Slide 4: Step2:install the frame
Pay attention please, don't make the back to front.

## Slide 5: Step3:fix the frame from bottom of base with screws: M5 X 12 2PCS

## Slide 6: Step4: install the leadrail of the X axis with screws: M3 X 30 8 PCS PS:please read STEP 5 as a reference

## Slide 7: Step5: Pay attention
if the leadrail is not level after you screw, please unscrew and adjust it to level.

## Slide 8: Step6: install T8-leadscrew
take the copper nut from
the T8-leadscrew

## Slide 9: Step7: Fix copper srew nut to the leadrail with: M3 X 8 4 PCS

## Slide 10: Step8: Install and fix T8 leadscrew to the coupler

## Slide 11: Step9:Pay attention
After you install the T8 leadscrew, please test if you
can turn the coupler to move the leadrail up and down.
Please turn both coupler at the same time from the very
bottom to very up. Usually, its very easy to be turnt.
if it's too tight to move, please stop turning and
refer to next step for adjusting. If it moves smoothly,
ignore step 10. Must pay attention to the fault
because it would cause the motor can't drive
the leadrail so that the printer can't work

## Slide 12: Step 10: Find the reason for the fault of step 9
Please check the screws one by one
to see if they are screwed too tight
Must pay attention to the fault
because it would cause the motor
can't drive the leadrail up so that the
printer can't work

## Slide 13: Step11: Fix the extruder holder to the X axis with screws: M3 X 8 4PCS
Don't make the back to front

## Slide 14: Step12:Install the extruder to X Axis with screws: M5 X 12 3PCS
Don't make the back to front

## Slide 15: Step13: Install stepper motor to the X Axis with screws: M3 X 8 4PCS

## Slide 16: Step14:Install belt to the X Axis: M3 X 8 4PCS

## Slide 17: Step15: Fix Turbofan with screws: M3 X 8 2PCS

## Slide 18: Step 16：Install X -ENDSTOP

## Slide 19: Step17：Install- X ENDSTOP
M3 X 8 2PCS

## Slide 20: Step18：Wiring of the Cooling Fan
Find No.1 (wire of 12V cooling fan)and connect it to the right position.
pay attention: Red to Red. Black to Black

## Slide 21: Step19：Wiring of the Turbofan
Find No.2 (12v turbofan) and connect it to right position
Pay attention: Red to Red. Black to Black

## Slide 22: Step20：Wiring of Heater
Find No.3(24v Heater) and connect it to the right position
Pay attention: Red to Red, Black to Black

## Slide 23: Step21：Wiring of the thermistor of hotend
Please find the thermistor of the hotend, and connect it to A13 of the Mainboard

## Slide 24: Step22：Wiring of the X-Axis stepper motor
please find the stepper motor of the X-Axis, and connect it to X_MOT of the Mainboard

## Slide 25: Step23：Wiring of the extruder stepper motor
Please find the stepper motor of the extruder, and connect it to E0_MOT of the Mainboard

## Slide 26: Step24: Install the Z-Axis ENDSTOP
Unscrew
ensure the small part touch the base
screw tight
complete

## Slide 27: Step25：Wiring of the Z-Axis endstop
connect them together

## Slide 28: Step26：Install heating bed and Y Axis
find the connector of the Y-Axis stepper and connect it to Y_MOT of the Mainboard

## Slide 29: Step27：Wiring of the Y-Axis stepper motor
Connect the Y-Axis stepper motor to Y_MOT of the Mainboard

## Slide 30: Step28：Wiring of the thermistor of the heatbed
Find the thermistor of the heatbed and connect it to A14 of the main board.
get it through the hole

## Slide 31: Step 29：Install the Y- Axis

## Slide 32: Step30：Install heatbed
注意热床的方向，以图作为标准

## Slide 33: Step31：Install heatbed
rescrew the four screws as before they were taken apart and then block them.

## Slide 34: Step32：install the heatbed
rescrew the four screws as before they were taken apart and then block them.

## Slide 35: Step33：Install Y-Axis endstop with: M3 X 8 2PCS

## Slide 36: Step 34：Wiring of the Y-Axis endstop

## Slide 37: Step35：Fix both acrylic frame
Fix the the frame with power supply: M5 X 12 7PCS

## Slide 38: Step 36：Install LCD in the top acrylic frame
connect the two wires with LCD first

## Slide 39: Step 37：Choose the correct voltage in the power supply. It's very important.
this step is very important. if you don't make the voltage correctly, it will cause printer burnt
after you finish previous installation, you should test the printer before you finish the rest installion.
But before testing, you must choose the correct the voltage first.
There is a voltage switch in the power supply. one side is 230v, one side is 115v. if your local voltage is 220v, please turn the switch to 230v side. if your local voltage is 110v, please turn the switch to 115v
side.

## Slide 40: Step 38：Test the printer
after you confirm the correct voltage, please let the printer power on. Working status would be: the fan works, LCD can display like the picture.

## Slide 41: Step39：Problems would occur while testing
no any characters in the LCD,
please ensure you have done correct wiring.
messing codes occur in the LCD, please press the buttoon
like the picture

## Slide 42: Step40：Test the endstop
Fix the printed part of Z axis endstop to the place as the pictures show
after fixing the printed part, please turn the screw to very bottom, which can ensure the hotend don't touch the heatbed

## Slide 43: Step 41：Test all endstops
test the endstop with lcd
1. press the button ->turn it to 'Prepare' and press ->turn the button to ' Auto home ' and press
X-Axis ENDSTOP is Auto home
Y-Axis ENDSTOP is Auto home
Z-Axis ENDSTOP is Auto home

## Slide 44: Step42：Install the top acrylic framce
Put M3 *20screws into the hole of top acrylic frame
fix the screws in the hole with tape

## Slide 45: Step 43：Install top acrylic frame
Fix top acrylic frame with M3*20 screws，ATTENTION：Acrylic frame is fragile, please screw it carefully

## Slide 46: Step44：Tie the wires

## Slide 47: Step 45：Testing and Calibration
level the heatbed through adjusting the 3 screws
distance between nozzle and headbed is the thickness of a pcs of A4 paper. Meanwhile, you can move the paper smoothly between them.